## Slide 1
Land Management and Land Use Planning
Dr. Susana Restrepo Rico
Urban Agglomerations Master of Science (M. Sc.)
Frankfurt UAS
WS 2025/26
Municipal Planning in Germany
From Spatial Strategies to Concrete Implementation

## Slide 2
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
GOVERNANCE LEVELS IN PLANNING PROCEDURES
Rechtsrahmen / Raumordnungsgesetzt
Legal framework / Spatial Planning Act
Landesentwicklungsplan / Landesplanungsgesetz
State Spatial Planning Act, State Development Plan
Regionalpläne / Regional Plans
Flächennutzungs- und Bebauungsplan
Land-Use Plan and Local Development Plan
Planning Instruments
Bundesministerien, Bundesinstitute, Bundestag/Bundesrat
Federal Ministries, Federal Institutes, Bundestag / Bundesrat
Landesministerien, Landesregierung
State Goverments
Regionale Planungsverbände, Regierungspräsidium
Regional Planning Associations, Regional Government
Stadtplanungsamt, Gemeinderat
City Planning Departments, Municipal Councils
Planning Actors
Actors in Participation
Länder, Fachministerien, Verbände
States, sectoral ministries, professional associations
Kommunen, Fachbehörden, Öffentlichkeit
Municipalities, sectoral agencies, public
Kommunen, Verbände, Bürger:innen
Municipalities, associations, citizens
Bürger:innen, Fachbehörden, Initiativen
Citizens, authorities, civic initiatives
Bundesebene
Federal Level
Landesebene
State Level
Regionale Ebene
Regional Level
Kommunale Ebene
Municipality Level
Governance Level

## Slide 3
Municipal Land-Use Planning in Germany
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Notes: Frankfurt uses B-Plans extensively to guide major transformations, e.g.:
Europaviertel-West / Europaviertel-Ost (B-Plan 826 & 850): mixed-use boulevard, height zoning, green axis
Rebstockpark (B-Plan 680+): residential quarters with structured block form
Schönhof-Viertel (B-Plan 899): conversion of former freight land into dense urban housing

## Slide 4
Municipal Land-Use Planning in Germany
Bauleitplanung = Municipal Land-Use Planning
Flächennutzungsplan (FNP)
Preparatory & binding plan for the entire municipality
Defines:
Housing areas
Commercial zones
Mixed-use corridors
Green corridors and fresh-air ventilation routes
Areas for high-rise development
Mobility axes
Infrastructure
The FNP sets the stage for Bebauungspläne (B-Plans) by defining where major development should occur e.g., Europaviertel, Gateway Gardens, Ostend
Frankfurt uses the Regionaler Flächennutzungsplan Rhein-Main (RPFNP) as its FNP
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Bebauungsplan (B-Plan)
Binding rules for specific development areas
B-Plans translate the FNP into legally binding rules, defining:
Type of building use (WA, MI, GE…)
density,
building heights
Street network
open spaces
mobility requirements
Environmental and climate adaptation measures
Frankfurt uses B-Plans extensively to guide major transformations, e.g.,Europaviertel-West / Europaviertel-Ost (B-Plan 826 & 850), Rebstockpark (B-Plan 680), Schönhof-Viertel (B-Plan 899)
Notes: Frankfurt uses B-Plans extensively to guide major transformations, e.g.:
Europaviertel-West / Europaviertel-Ost (B-Plan 826 & 850): mixed-use boulevard, height zoning, green axis
Rebstockpark (B-Plan 680+): residential quarters with structured block form
Schönhof-Viertel (B-Plan 899): conversion of former freight land into dense urban housing

## Slide 5
Bauleitplanung
Flächennutzungsplan (FNP)
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Notes: Frankfurt uses B-Plans extensively to guide major transformations, e.g.:
Europaviertel-West / Europaviertel-Ost (B-Plan 826 & 850): mixed-use boulevard, height zoning, green axis
Rebstockpark (B-Plan 680+): residential quarters with structured block form
Schönhof-Viertel (B-Plan 899): conversion of former freight land into dense urban housing

## Slide 6
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Bebauungsplan (B-Plan) Europaviertel West/Ost
Bauleitplanung

## Slide 7
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
B-Plan
Regulates development at the parcel and block level
Adopted as a municipal statute by the city council
Directly governs what may and may not be built
Typical Elements:
Type of building use (Art der baulichen Nutzung): WA = residential, MI = mixed-use, GE = commercial, SO = special zones
Density & dimensions (Maß der Nutzung): GFZ (floor area ratio), GRZ (site coverage), Maximum building heights & storeys
Urban form: Building lines, footprints, block structure
Street layout & public squares
Green & environmental requirements: Trees, unsealed surfaces, noise protection, flood rules
Mobility: Road hierarchy, cycle paths, pedestrian routes
Public transport corridors (U5 in Europaviertel)
The B-Plan transforms urban strategy into a legally enforceable design
Bauleitplanung - Bebauungsplan
Notes: What is GRZ? (Grundflächenzahl)
o” = Oberste Geschossart top storey (or the roof form) must be executed as a geschoss mit Dachform, meaning a roof-shaped or attic-like storey, often a “staffelgeschoss” or pitched-roof zone.
“a”: The attic may be usable (ausgebaut). It may contain living space. It may have roof windows or dormers. It still must follow the roof geometry defined in the textual B-Plan. It cannot visually or volumetrically behave like a full regular storey.

## Slide 8
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
WA – Allgemeines Wohngebiet (Residential Area)
Primarily housing
Allowed uses:
Residential buildings
Daycare
Small shops
Small offices
Social infrastructure
Noise-sensitive uses are protected
Urban effect
Quiet residential environment
Structured block forms or open housing layouts, depending on GRZ/GFZ
B-Plan - Type of building use (Art der baulichen Nutzung)
Notes: What is GRZ? (Grundflächenzahl)
o” = Oberste Geschossart top storey (or the roof form) must be executed as a geschoss mit Dachform, meaning a roof-shaped or attic-like storey, often a “staffelgeschoss” or pitched-roof zone.
“a”: The attic may be usable (ausgebaut). It may contain living space. It may have roof windows or dormers. It still must follow the roof geometry defined in the textual B-Plan. It cannot visually or volumetrically behave like a full regular storey.

## Slide 9
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
MI – Mischgebiet (Mixed-Use Area)
Balanced mix of housing + commercial
Allowed uses:
Housing
Shops, cafés, restaurants, offices
Small production and service businesses
Urban effect:
Active ground floors
More noise tolerated“City life”
B-Plan - Type of building use (Art der baulichen Nutzung)
Notes: What is GRZ? (Grundflächenzahl)
o” = Oberste Geschossart top storey (or the roof form) must be executed as a geschoss mit Dachform, meaning a roof-shaped or attic-like storey, often a “staffelgeschoss” or pitched-roof zone.
“a”: The attic may be usable (ausgebaut). It may contain living space. It may have roof windows or dormers. It still must follow the roof geometry defined in the textual B-Plan. It cannot visually or volumetrically behave like a full regular storey.

## Slide 10
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
GE – Gewerbegebiet (Commercial/Industrial Zone)
Work & production-oriented uses
Allowed uses:
Industrial
Logistics
Wholesale
Workshops
Offices
Commercial operations
Housing usually prohibited (to avoid conflicts)
Urban effect:
Large commercial structures
Transport access
Low walkability
Higher noise/emission tolerance
B-Plan - Type of building use (Art der baulichen Nutzung)
Notes: What is GRZ? (Grundflächenzahl)
o” = Oberste Geschossart top storey (or the roof form) must be executed as a geschoss mit Dachform, meaning a roof-shaped or attic-like storey, often a “staffelgeschoss” or pitched-roof zone.
“a”: The attic may be usable (ausgebaut). It may contain living space. It may have roof windows or dormers. It still must follow the roof geometry defined in the textual B-Plan. It cannot visually or volumetrically behave like a full regular storey.

## Slide 11
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
SO – Sondergebiet (Special-Purpose Zone)
Unique or large-scale functions not covered by standard categories
Examples:
Shopping centres
University
Hospital
Airports
Major institutions
Urban effect:
Strong identity
Landmark buildings
Tailored regulations to specific uses
B-Plan - Type of building use (Art der baulichen Nutzung)
Notes: What is GRZ? (Grundflächenzahl)
o” = Oberste Geschossart top storey (or the roof form) must be executed as a geschoss mit Dachform, meaning a roof-shaped or attic-like storey, often a “staffelgeschoss” or pitched-roof zone.
“a”: The attic may be usable (ausgebaut). It may contain living space. It may have roof windows or dormers. It still must follow the roof geometry defined in the textual B-Plan. It cannot visually or volumetrically behave like a full regular storey.

## Slide 12
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
GRZ – Grundflächenzahl (Site Coverage Ratio)
What it means: How much of the plot area you are allowed to cover with the building footprint.
GRZ Counts:
The principal building footprint
Fixed structural extensions, e.g., Winter gardens (if structural)
Fixed verandas that are part of the main building geometry
Formula:
GRZ x plot area = maximum ground coverage
Urban effect:
Low GRZ (0.2–0.4): more gardens, more suburban or open development
Medium GRZ (0.4–0.6): structured blocks with courtyards
High GRZ (0.6–0.8): compact urban areas, less open ground
B-Plan – Density & Dimensions (Maß der Baulichen Nutzung)
Notes: GRZ Does NOT Count (excluded), Unless the B-Plan explicitly says otherwise, these DO NOT count toward GRZ: Terraces (open, unroofed) Balconies Driveways / paths, Pergolas without a roof, Open garden areas, Green roofs or planted surfaces, Parking spaces (unpaved or permeable)

## Slide 13
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
GFZ – Geschossflächenzahl (Floor Area Ratio / FAR)
How much total usable floor area you may build across all storeys.
Included in GFZ (always):
All full storeys above ground
Attic storeys if they qualify as Vollgeschosse
Roof storeys if they exceed the “Dachgeschoss exemption rule”
Stair cores
Lift shafts
Technical rooms (above ground)
Internal corridors
Formula:
GFZ x plot area = total permitted floor area.
Urban effect:
GFZ < 1.0: suburban, low density
GFZ 1.0–1.7: typical 3–5 storey European neighborhoods
GFZ 2.0–3.0: inner-city blocks (Frankfurt Bornheim, Teile Europaviertel)
GFZ 4.0+ (rare): high-rise clusters (some SO or core MI areas)
B-Plan – Density & Dimensions (Maß der Baulichen Nutzung)
Notes: Not included (usually): (but depends on B-Plan text — important for Frankfurt!) Basement floors (unless partially above natural ground level) Loggias / balconies. Open arcades. Underground garages. Terraces. Roof terraces
Big nuance: A roof storey may or may not count as a Vollgeschoss. The definition of Vollgeschoss is highly regulated (BauO Hessen §2). If it's not a Vollgeschoss, its floor area usually does not count toward GFZ.
Vollgeschosse (full storeys): The three lower floors with vertical walls. Dachgeschoss (roof storey): The uppermost floor partially under the sloped roof. This is not always counted as a full storey — depends on roof angle & usable area (BauO Hessen rules).

## Slide 14
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Maximum Building Heights & Storeys (Höhenbegrenzung & Vollgeschosse)
Storeys (Vollgeschosse): Written in the B-Plan as: II, III, IV, V, etc.
Sometimes combined with symbols:
III o = 3 full floors + roof-shaped top storey
III a = 3 full floors + developed attic
Urban effect:
Controls perceived scale from the street
Ensures harmonious transitions to existing neighbourhoods
Limits overshadowing and wind effects
B-Plans may specify:
Maximum ridge height (Firsthöhe): from the starting of the roof to the highes point of the building
Maximum eaves height (Traufhöhe): From the floor to the beginning of the roof line
Absolute maximum building height: Gebäudehöhe (full height)
B-Plan – Density & Dimensions (Maß der Baulichen Nutzung)

## Slide 15
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Building Lines (Baulinien)
A Baulinie marks the exact line on which a building’s façade must be placed:
Strict, no setback allowed
Façade must align exactly with this line
How it appears in a B-Plan
Solid line (often red or blue) along a street edge
Urban Effect:
Creates coherent street walls
Defines the urban profile
Controls street enclosure and “city feel”
Ensures architectural continuity (e.g., Europa-Allee)
B-Plan – Urban Form

## Slide 16
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Building Footprints (Baufenster / Baugrenzen)
Defined through Baugrenzen (building limits) or Baufenster (buildable envelopes)
Inside the polygon: the building may be placed.
Outside: the building may not encroach.
How it appears in a B-Plan:
Dashed lines marking the maximum area for construction.
The shape usually anticipates the intended block typology.
What it regulates:
Mass building depth, and courtyard sizes
Distances to neighbours
Protection of sunlight and ventilation
Control of block typology (open, semi-open, or perimeter block)
B-Plan – Urban Form

## Slide 17
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Block Structure (Blockrand vs. offene Bauweise)
The overall shape of development:
Closed blocks
Semi-open blocks
Freestanding buildings
How it appears in a B-Plan:
Baufenster and Baulinien together outline a block perimeter.
Use category (WA/MI) and GFZ help define massing.
What it regulates:
Urban density & character
Degree of permeability (public vs private courtyard)
Noise shielding (closed blocks protect inner courtyards)
Microclimate (ventilation, shading)
B-Plan – Urban Form

## Slide 18
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Street Layout & Public Squares
How streets & squares appear in a B-Plan
Marked as öffentliche Verkehrsflächen (public traffic areas)
Coloured yellow/grey depending on local conventions
Public squares often marked with special symbols or labels
What the B-Plan regulates:
Street hierarchy: main, collector, local
Widths of carriageways, footpaths, cycle paths
Junctions, turning areas, and access points
Location & size of public squares
Ensures future development fits a coherent mobility and public-space structure
B-Plan – Urban Form

## Slide 19
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Green & Environmental Requirements
How they appear in a B-Plan:
Green areas often coloured green
Required tree planting shown with symbols
Noise protection walls indicated with thick lines
Flood zones hatched or labelled
Unsealed/permeable surfaces specified in text
What they regulate:
Tree planting requirements (species, number, spacing)
Green corridors and ecological connections
Unsealed surface quotas for climate resilience
Noise buffers (e.g., near rail lines or highways)
Flood rules: Prohibition of basements
Minimum elevation of ground floors
Retention or infiltration measures
B-Plan – Urban Form

## Slide 20
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Mobility: Road Hierarchy, Cycling, Pedestrian Routes, Public Transport
How mobility appears in a B-Plan:
Roads marked as Verkehrsflächen
Cycle paths shown as line symbols or shaded strips
Pedestrian routes as dotted or narrow access paths
PT corridors marked with “ÖPNV-Trasse” or special hatchings
What it regulates
Road hierarchy: Primary roads, collector roads, local streets
Access restrictions and turning radii
Cycle paths: Exact alignment & width; separation from car traffic
Pedestrian routes: Through-block passages; public vs semi-public accessibility; connections to squares, parks, and transit
Public Transport Corridors: space for future infrastructure; station entrances and underground alignments protected; prevents construction on top of critical transport corridors
B-Plan – Urban Form

## Slide 21
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Activity
Analyse ALL Three B-Plans Using the Guiding Questions (20 Minutes)
Pairs work through each of the three B-Plans and answer the following:
What does this B-Plan allow and restrict? (Use: WA/MI/GE/SO + density + height)
2. What urban form does it produce? (Use: Baulinien, Baufenster, block structure)
3. How does the street & mobility network work? (Use: hierarchy, cycle paths, pedestrian routes, PT corridors)
4. How are environment & climate addressed? (Use: trees, unsealed surfaces, noise protection, flood zones)
5. What type of neighbourhood will emerge here? (Residential? Lively mixed-use? Industrial? Family-oriented? Dense, urban? etc.)
B-Plan

## Slide 22
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
B-Plan

## Slide 23
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
B-Plan

## Slide 24
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
B-Plan

## Slide 25
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Land Management and Land Use Planning
Dr. Susana Restrepo Rico
Urban Agglomerations Master of Science (M. Sc.)
Frankfurt UAS
WS 2025/26
From Draft to Law: The Bebauungsplan Approval Process in Germany

## Slide 26
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
The Legal Framework
The preparation and approval of a Bebauungsplan are governed by the German Federal Building Code (Baugesetzbuch, BauGB).
The B-Plan is the most detailed land-use regulation instrument available to municipalities and must comply with the hierarchy of planning instruments.
Key legal foundations from the BauGB:
BauGB §§ 1–4: Define planning objectives, public interest obligations, and the required participation of citizens and authorities.
BauGB § 2: Grants municipalities the authority to initiate planning procedures independently.
BauGB §§ 3 and 4: Establish the mandatory steps for public participation and involvement of authorities.
BauGB §§ 8–10: Regulate the preparation, adoption, and legal effectiveness of the Bebauungsplan as a municipal statute.
EU Strategic Environmental Assessment Directive: Requires a formal environmental assessment (Umweltprüfung) for all plans with potential environmental effects.
The legal framework ensures transparency, democratic legitimacy, and environmental protection throughout the planning process
Bebauungsplan Process
Preparation
Preliminary Draft
Statue / Law
Draft

## Slide 27
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Preparation
A Bebauungsplan begins with a formal decision by the municipality to start the planning process.
This step establishes the planning mandate and defines the scope of work.
The planning impulse may come from:
Political bodies seeking urban development or renewal.
Municipal departments identifying infrastructural or environmental needs.
Private developers requesting planning rights for specific projects.
Public institutions needing land for facilities or services.
The city administration prepares a preliminary assessment outlining:
Planning objectives and desired urban development outcomes.
The boundary of the planning area.
Key issues requiring analysis, such as land use, density, mobility, environmental impact, and infrastructure.
The need for specialised studies.
The procedure formally begins with the Aufstellungsbeschluss adopted by the City Council (Stadtverordnetenversammlung).
Bebauungsplan Process
1. Initiation of the Planning Procedure
2. Resolution to Prepare the Bebauungsplan (Aufstellungsbeschluss)
3. Preliminary Draft (Vorentwurf)
4. Early Participation of the Public and Authorities
5. Resolution to Publish the Draft (Auslegungsbeschluss)
6. Public Display and Participation of Authorities
7. Resolution to Adopt the Bebauungsplan
8. Approval (if required)
9. Official Announcement and Entry into Force
Preparation

## Slide 28
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Preliminary Draft
The municipality develops the first comprehensive concept for the plan area.
The Vorentwurf has the following functions:
It translates the planning objectives established in the initiation phase into a spatial concept.
It outlines initial land-use categories such as residential, mixed-use, commercial, or special designations.
It defines preliminary density and building form guidelines, for example possible GRZ, GFZ, and storey limits.
It shapes the first version of the street network, access points, and mobility framework.
It identifies potential locations for green spaces, ecological compensation areas, and public facilities.
It sets the scope for the environmental assessment by indicating expected environmental impacts and required studies.
Inter-departmental collaboration happens during this step.
Specialised departments such as environment, mobility, water and wastewater, nature conservation, and heritage preservation review the preliminary concept and provide technical input.
The Vorentwurf is not yet binding
Bebauungsplan Process
1. Initiation of the Planning Procedure
2. Resolution to Prepare the Bebauungsplan (Aufstellungsbeschluss)
3. Preliminary Draft (Vorentwurf)
4. Early Participation of the Public and Authorities
5. Resolution to Publish the Draft (Auslegungsbeschluss)
6. Public Display and Participation of Authorities
7. Resolution to Adopt the Bebauungsplan
8. Approval (if required)
9. Official Announcement and Entry into Force
Preliminary Draft

## Slide 29
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Preliminary Draft – Vorentwurf
Who develops the Vorentwurf?
The legal responsibility always lies with the municipality:
Initiates the B-Plan procedure.
Prepares and determines the content of the B-Plan.
Performs the balancing (Abwägung).
Adopts the plan as a statute.
This legal responsibility cannot be transferred to a private developer, but private developers can prepare a draft concept or Vorentwurf-like materials.
Project-driven B-Plans
Investor-funded B-Plan or project-driven B-Plan.
The developer finances the preparation of planning documents:
Urban design studies
Feasibility studies
Preliminary layouts
Conceptual massing plans
Environmental pre-assessments
These documents can serve as the basis for the municipal Vorentwurf
The municipality must review them, modify them according to public interest, and integrate them into its planning goals.
Bebauungsplan Process
Notes: Consultants hired by the developer may produce the initial draft.But again:The planning sovereignty (Planungshoheit) remains fully with the municipality.The municipality is the one who creates the official Vorentwurf and the official Planentwurf.Only the municipality can decide which parts of the developer’s proposal become part of the B-Plan.4. Why the municipality must remain responsibleBauGB requires:Public participationAuthority participationEnvironmental assessmentBalancing of interestsPolitical adoptionThese steps require neutrality.A private developer cannot fulfil these legal obligations because they represent private interests, not the public good.5. Summary suitable for your slideHere is a perfectly concise version you can use in your lecture:“The Vorentwurf is formally prepared by the municipality. Developers may submit concept drafts or urban design studies that the municipality can use as a basis, but the planning sovereignty and the legal responsibility for the content remain exclusively with the municipality.”

## Slide 30
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Early Public Participation
Identify concerns, conflicts, and opportunities early in the planning process.
Early public (civic) participation includes:
Providing information about the Vorentwurf in accessible formats, such as local exhibitions, online platforms, presentations, or neighbourhood meetings.
Giving residents and affected stakeholders the opportunity to express concerns, ideas, or objections.
Collecting local knowledge that may not be available through technical studies.
Documenting all comments for later evaluation.
Early authority participation includes:
Consulting technical agencies, public-interest bodies, and service providers.
Identifying technical constraints such as flood risk, noise exposure, infrastructure capacity, soil conditions, or conservation requirements, etc.
Receiving expert feedback that informs the refinement of the B-Plan.
Prepare for the legally binding public display phase that comes later in the process. This stage serves as the bridge between the preliminary design and the formal B-Plan draft.
Bebauungsplan Process
1. Initiation of the Planning Procedure
2. Resolution to Prepare the Bebauungsplan (Aufstellungsbeschluss)
3. Preliminary Draft (Vorentwurf)
4. Early Participation of the Public and Authorities
5. Resolution to Publish the Draft (Auslegungsbeschluss)
6. Public Display and Participation of Authorities
7. Resolution to Adopt the Bebauungsplan
8. Approval (if required)
9. Official Announcement and Entry into Force
Preliminary Draft

## Slide 31
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Early Public Participation
Participation at this stage is informal but legally required under BauGB.
Actors typically involved:
Residents and property owners
Local inhabitants.
Neighbouring communities and affected stakeholders
Individuals or groups who may be indirectly affected, including adjacent landowners, businesses, or community organisations.
Civil society organisations.
Associations and interest groups representing environmental, cultural, mobility, or heritage concerns.
Developers and investors
Participation formats:
Public exhibitions and information events
Display boards, online documents, and explanatory sessions.
Workshops and discussion forums.
Online platforms and digital feedback tools
Written submissions
Bebauungsplan Process

## Slide 32
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Resolution to Publish the Draft
After incorporating feedback from early participation and adjusting the preliminary draft, the municipality prepares the formal B-Plan draft.
Before this draft can be released to the public for the statutory display period, the City Council or designated planning committee must adopt the Auslegungsbeschluss.
The Auslegungsbeschluss authorises:
The publication of the full B-Plan draft, including plan drawing, textual regulations, justification, and environmental report.
The scheduling of the statutory public display
The parallel involvement of authorities
This step:
Ensures that the draft has been sufficiently prepared to withstand formal participation.
Confirms political support for advancing the plan.
Secures procedural correctness before entering the most legally sensitive phase.
The Auslegungsbeschluss marks the transition from the informal, exploratory phase to the formal, legally binding consultation procedure.
Bebauungsplan Process
1. Initiation of the Planning Procedure
2. Resolution to Prepare the Bebauungsplan (Aufstellungsbeschluss)
3. Preliminary Draft (Vorentwurf)
4. Early Participation of the Public and Authorities
5. Resolution to Publish the Draft (Auslegungsbeschluss)
6. Public Display and Participation of Authorities
7. Resolution to Adopt the Bebauungsplan
8. Approval (if required)
9. Official Announcement and Entry into Force
Draft

## Slide 33
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Public Display and Formal Public Participation
This is a legally binding participation step and must follow strict procedural requirements
.The municipality publishes:
The plan drawing (Planzeichnung)
Textual regulations (Festsetzungen)
The justification (Begründung)
The Environmental Report (Umweltbericht)
Any additional technical documents relevant for assessment.
The documents must be made available for a minimum of one month.
Access must be provided both in the planning department and, increasingly, through online platforms.
During this period:
Residents, businesses, and other stakeholders may submit written comments or objections.
All submissions must be accepted without restrictions, regardless of content or format.
The municipality is required to document every statement received.
Bebauungsplan Process
1. Initiation of the Planning Procedure
2. Resolution to Prepare the Bebauungsplan (Aufstellungsbeschluss)
3. Preliminary Draft (Vorentwurf)
4. Early Participation of the Public and Authorities
5. Resolution to Publish the Draft (Auslegungsbeschluss)
6. Public Display and Participation of Authorities
7. Resolution to Adopt the Bebauungsplan
8. Approval (if required)
9. Official Announcement and Entry into Force
Draft

## Slide 34
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Public Display and Formal Public Participation
Participation during this stage is formal, documented, and legally binding.
Actors involved:
Residents and property owners.
Businesses and institutions: Local shops, service providers, schools, or social facilities may assess implications for logistics, accessibility, or neighbourhood functions.
Developers and investors: Companies holding land within or near the B-Plan area may analyse development rights, feasibility, and regulatory constraints.
Civil society organisations: Environmental groups, mobility advocates, heritage organisations, neighbourhood associations, or professional bodies provide thematic feedback and formal objections.
General public: Any individual, regardless of residence or ownership status, has the right to submit comments.
Participation formats:
Reading-room consultation (Auslegung im Rathaus: Documents are physically displayed in the municipal planning office.
Online publication (digitale Auslegung): Enables broader access and remote participation.
Written submissions.
Bebauungsplan Process

## Slide 35
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Resolution to Adopt the Bebauungsplan (Satzungsbeschluss)
Once all comments from the public and authorities have been evaluated and incorporated into the final draft, the municipality prepares the Satzungsbeschluss, the formal resolution to adopt the Bebauungsplan.
The Satzungsbeschluss is made by the City Council (Stadtverordnetenversammlung) or the competent municipal body.
With this resolution, the B-Plan becomes a municipal statute (“Satzung”).
Requirements before adoption:
Completion of the public display and formal participation procedures.
Proper documentation and balancing of all comments (Abwägung).
A finalised plan drawing, textual regulations, justification, and environmental report.
Confirmation that the draft complies with higher-level planning instruments (Regionalplan, FNP) and legal requirements.
Provides democratic legitimacy for the B-Plan.
Enable the B-Plan to guide and control future development.
Bebauungsplan Process
1. Initiation of the Planning Procedure
2. Resolution to Prepare the Bebauungsplan (Aufstellungsbeschluss)
3. Preliminary Draft (Vorentwurf)
4. Early Participation of the Public and Authorities
5. Resolution to Publish the Draft (Auslegungsbeschluss)
6. Public Display and Participation of Authorities
7. Resolution to Adopt the Bebauungsplan
8. Approval (if required)
9. Official Announcement and Entry into Force
Statute / Law

## Slide 36
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Approval of the Bebauungsplan (Genehmigung, if required)
After the municipality adopts the Bebauungsplan as a statute (Satzungsbeschluss), an external approval step may be required depending on the federal state and the legal status of the municipality.
Approval may be necessary when:
The municipality does not have planning sovereignty or operates under supervisory oversight.
The B-Plan requires exemption or deviation from higher-level planning instruments.
Certain public authorities must confirm compliance with specialised regulations (such as water law, flood protection, or nature conservation) before the plan becomes effective.
If approval is required, the supervisory authority issues a formal notification (Genehmigungsbescheid).
If no approval is required, the municipality proceeds directly to the official announcement of the plan.
Bebauungsplan Process
1. Initiation of the Planning Procedure
2. Resolution to Prepare the Bebauungsplan (Aufstellungsbeschluss)
3. Preliminary Draft (Vorentwurf)
4. Early Participation of the Public and Authorities
5. Resolution to Publish the Draft (Auslegungsbeschluss)
6. Public Display and Participation of Authorities
7. Resolution to Adopt the Bebauungsplan
8. Approval (if required)
9. Official Announcement and Entry into Force
Statute / Law
Notes: In most cities, including Fra
Ensures that the B-Plan complies with federal and state law.
Verifies consistency with the Regional Plan and the Flächennutzungsplan.
Confirms that all procedural requirements under BauGB have been fulfilled correctly.
Protects against procedural or legal errors that could invalidate the plan.
nkfurt, approval is not required because municipalities possess full planning competence (Planungshoheit).However,

## Slide 37
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Official Announcement and Entry into Force
The plan becomes legally binding only upon its official publication in the municipal gazette (Amtsblatt) or another authorised publication medium.
The announcement must include:
A reference to the adopted B-Plan and the date of its resolution.Information on where and how the plan can be inspected (Step 7).
A notice of legal remedies, specifying how and within what period objections or challenges may be raised.
Entry into force:
The Bebauungsplan comes into legal effect on the day the announcement is published.
From this moment, all future building permits and land-use decisions must comply with the plan.
The B-Plan becomes binding on both private individuals and public authorities.
Bebauungsplan Process
1. Initiation of the Planning Procedure
2. Resolution to Prepare the Bebauungsplan (Aufstellungsbeschluss)
3. Preliminary Draft (Vorentwurf)
4. Early Participation of the Public and Authorities
5. Resolution to Publish the Draft (Auslegungsbeschluss)
6. Public Display and Participation of Authorities
7. Resolution to Adopt the Bebauungsplan
8. Approval (if required)
9. Official Announcement and Entry into Force
Statute / Law

## Slide 38
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Challenges in the Bebauungsplan Process
Typical challenges:
Balancing conflicting interest (Abwägungsprozess)
Lengthy procedures and administrative complexity
Extended timelines, particularly in larger cities.
Coordination across multiple authorities.
Conflicting technical requirements.
Public objections and political debates.
Political decision-making can delay or reshape the plan.
Environmental and technical constraints
Legal vulnerability.
Resource limitations.
The cumulative effect of these challenges explains why the B-Plan procedure requires careful management, extensive coordination, and significant time.
Bebauungsplan Process
Notes: Although the Bebauung
Balancing conflicting interest: The legally required balancing process (Abwägung) can be highly sensitive.
Lengthy procedures and administrative complexity: The B-Plan process involves many actors, formal steps, and detailed documentation requirements under the BauGB.
Extended timelines, particularly in larger cities.
Coordination across multiple authorities: Environmental, transport, water, energy, heritage, and safety agencies must be consulted.
Conflicting technical requirements may require repeated revisions.
Public objections and political debates: Residents and stakeholders may raise concerns about density, noise, traffic, environmental impacts, or property values.
Political decision-making can delay or reshape the plan.
Environmental and technical constraints
Legal vulnerability: Errors in public participation, documentation, or the balancing of interests can lead to legal challenges, causing delays or invalidation of the entire plan.
Resource limitations: Municipal planning departments often face staff shortages and high workloads, which can slow down plan preparation.
splan provides legal certainty and transparent planning, its preparation is often complex and time-consuming

## Slide 39
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Planning as a Shared Responsibility
The preparation of a Bebauungsplan is more than a legal procedure. It is a collective process through which municipalities, experts, stakeholders, and residents shape the future of their city.
Each stage of the procedure, analysis, design, participation, balancing, and adoption, reflects the interplay between public interest, technical expertise, and democratic negotiation.
Urban planning is not only about regulations but about creating places that support everyday life, environmental quality, and long-term social cohesion.
A legally binding plan is the outcome of many decisions, dialogues, and compromises, and its value lies in transforming spatial concepts into real urban environments.
Good planning requires transparency, cooperation, and a shared commitment to the city’s future.
Bebauungsplan Process

## Slide 40
Dr.-Ing. Susana Restrepo Rico
Urban Agglomerations M.Sc.
Questions?
Bebauungsplan Process